## Slide 1: RA 2025 Demand Forecasting Update
Lynn Marshall, Energy Assessments Division, CEC
Lynn.Marshall@energy.ca.gov
Slice of Day Office Hours, August 16, 2024

## Slide 2: RA 2025 Load Forecast Update
1. Review Forecast Adjustment Steps
  LSEs received workbooks with itemized forecast adjustments:
    Submitted Forecast
    LSE-Specific Adjustment
    Transmission & UFE Losses
    Coincidence Adjustment
    Load Credits
    LSE Type Pro-Rata
    Pro-Rata Adjustment
    Final Adjusted Forecast
2. Month Ahead Load Migration Template

## Slide 3: Submitted versus CEC Forecast Jan.-June 2025

## Slide 4: Submitted versus CEC Forecast July-Dec. 2025

## Slide 5: LSE-Specific Adjustments
The submitted monthly forecast is compared to a CEC benchmark:
  CEC estimates a reference monthly peak demand and peak-day energy for each LSE to evaluate need for LSE-specific adjustments.
  Apply curve-fitting formula to fit LSE’s submitted load shape to the target noncoincident monthly peak and energy.
Additional hourly adjustments were calculated by comparing the adjusted forecast to LSE recorded loads on high load days, taking into account load migration.
    These adjustments mostly focused on afternoon ramp hours.
  .

## Slide 6: Transmission & UFE Losses
Transmission loss factors were decided in a past RA decision to be 2.5%
PG&E is also adjusted by .5% for unaccounted for energy.
For SOD, transmission losses were added during the CAISO-defined Availability Assessment Hours for 2025:

## Slide 7: Coincidence Adjustment
CEC started with an estimate of total monthly coincidence, as in the past. This is a measure of total diversity within a month and is not hour-specific:
  Total Coincidence Factor (CF) =LSE load during high system load hours/LSE monthly peak.
Submitted forecasts already include within-day coincidence, but not across-month.
  Residual CF=Total CF – coincidence embedded in LSE forecast, including CEC adjustments.
    If this value is negative, indicates need for further LSE-specific adjustments.
  Hourly coincidence factor =Total CF – embedded CF
    This is applied to the sum of the submitted forecast, LSE-specific adjustments, and losses.

## Slide 8: Load Credits
Load credits are designated by CPUC decisions and include:
  LSE share of incremental PGC funded program impacts in the CEC forecast, net of impacts included in LSE’s submitted forecast.
  Credit for SCE IFOM storage discharge in non-summer months; credit is negative in off-peak hours to account for charging.
  Eligible LMDR.

## Slide 9: LSE Type and Final Pro-Rata
After applying the LSE-specific and coincidence adjustments, significant differences between adjusted load and the reference forecast remained, both positive and negative, most notably during solar production hours.
  Applying the resulting pro rata adjustments would produce abnormal load shapes for LSEs with minimal BTM PV.
  Staff constructed separate reference forecasts for Direct Access and non-Direct Access load and implemented an intermediate pro-rata step to within 5% of the type reference forecast.
Final step is pro-rata to within 1% of 2023 IEPR Planning Scenario 1-in-2 hourly forecast for the day of the monthly system peak day, by TAC.

## Slide 10: Coincident Peak Hour Forecast Adjustment Summary

## Slide 11: July 2025 Aggregate Adjusted Forecasts
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Submitted | 23896.86 | 22286.39 | 21139.96 | 20568.24 | 20787.04 | 21549.78 | 22659.91 | 23681.16 | 24508.48 | 25386.21 | 26489.5 | 27794.87 | 29294.65 | 30878.88 | 32635.57 | 34157.95 | 35532.23 | 36555.11 | 36531.74 | 35558.1 | 34152.77 | 32252.15 | 29155.51 | 26337.91
LSE-Specfic Adjustment | 1349.3213 | 1150.9119 | 1119.6533 | 1268.2136 | 1419.6514 | 1611.8301 | 1867.1964 | 1969.31 | 2008.5439 | 1963.7792 | 2140.4584 | 2276.8803 | 2751.5034 | 3717.1119 | 4145.8947 | 4162.4367 | 3673.7392 | 2941.9208 | 2037.0841 | 1703.0374 | 1650.1791 | 1118.4326 | 1132.1307 | 1173.3746
Net Losses, Coincidence, and Credits | -70.241 | -72.7061 | -76.3866 | -72.66 | -76.8739 | -82.9594 | -98.1519 | -132.0942 | -169.4962 | -204.8754 | -233.8027 | -263.4101 | -281.1442 | -276.1529 | -278.2583 | -272.4153 | 198.4192 | 229.4854 | 249.939 | 264.3764 | 268.802 | -104.5644 | -101.4687 | -89.5331
LSE Type Pro-Rata | 393.2096 | 365.6732 | 373.8259 | 461.8456 | 551.4192 | 650.5144 | 679.7451 | 591.1054 | 451.7829 | 363.9196 | 224.2344 | 167.373 | 288.6803 | 997.5464 | 1311.9106 | 1523.2882 | 774.9884 | 559.7258 | 842.9686 | 92.1055 | 0 | 100.2853 | -55.0785 | 154.6734
Final Pro-Rata Adjustment | 460.3192 | 451.9147 | 523.3952 | 538.5644 | 750.6228 | 880.173 | 962.2539 | 869.1862 | 566.8024 | 550.8584 | 632.1604 | 744.1066 | 1066.0241 | 1240.2637 | 1355.5833 | 1441.0016 | 1428.8376 | 1189.4756 | 1092.4793 | 965.1579 | 800.229 | 400.4425 | 373.7107 | 453.4436

## Slide 12: February 2025 Aggregate Adjusted Forecasts

## Slide 13: Month Ahead Load Forecast Template
Template will have 3 parts:
LSEs provide noncoincident peak day hourly profile of the aggregate of migrating load, by LSE type:
  DA versus IOU/CCA customers
SOD hourly calculations:
  Applies adjustments for coincidence and transmission losses.
Coincident and noncoincident peaks are extracted from 2), for CAISO RA and CRR reporting.

## Slide 14: Coincidence Factors by LSE Type for Month Ahead Forecast Template
Factors were estimated based on the aggregate of LSE type historic load and adjusted forecasts.

## Slide 15: Final Forecast Distribution
CEC plans to distribute to LSEs in early September:
  Final hourly and monthly coincident peak forecasts
  Month Ahead Load Migration template
Tables shown here will be posted on CPUC RA website.
Please contact CEC staff if you would like to discuss specifics of your forecast.