## Slide 1: CLECA Comments on Developing TOU Periods
Barbara R. Barkovich, Ph.D.
Barkovich & Yap, Inc.
Consultants to the California Large Energy Consumers Association
February 26, 2016

## Slide 2: Importance of Cost in Defining TOU Periods
Historically, TOU periods have been created by looking at the cost to serve customers during different hours of each year and grouping periods of similar costs
Generation-related costs
  For energy costs, study marginal energy costs, including wholesale energy prices, based on production cost modeling or other forecasting methods
  For generation capacity costs, assign marginal cost of capacity to each hour using loss of load probability, peak capacity allocation factors or some other adopted methodology
    most hours have zero generation capacity cost
  Combine generation energy and capacity costs for each hour to produce marginal generation cost
Distribution-related costs
  If these vary by hour, conduct similar analysis to that performed for generation capacity costs
Aggregate hours of similar costs into TOU periods varying by season
  If costs differ between weekends and weekdays, weekends may have no peak periods

## Slide 3: Monthly Average Marginal Generation Cost: Summer Weekdays versus Summer Weekends

## Slide 4: Monthly Average Marginal Generation Cost: Winter Weekdays versus Winter Weekends

## Slide 5: Use of Net Loads to Create TOU Periods
Net loads should only be used to develop TOU periods if these accurately reflect variations in costs
However, net load periods can show if current hourly and TOU costing needs revision
Most important is to study relationship between costs and net loads
In its 2015 RDW, PG&E studied historical as well as forecast raw loads, net loads and adjusted net loads and wholesale market prices
  Provided evidence that cost patterns were better predicted by adjusted net loads (net of hydro and nuclear as well as wind and solar); ORA confirmed
  See charts on next page
Similar analysis required for other utilities
Analysis should also be performed for distribution costs and loads

## Slide 6: Summer Weekday Preliminary TOU Analysis: Box Denotes Higher Cost Period

## Slide 7: Winter Weekday Preliminary TOU Analysis: Boxes Denote Higher Cost Periods

## Slide 8: Other Considerations
Consider implications of patterns of day ahead vs. real time wholesale prices
Use TOU rates to send price signals on a forward-looking basis
Give customers advance notice of TOU period changes
Retain TOU periods for two GRC cycles unless dramatic change in cost patterns
Minimize complexity
Consider options of narrower TOU periods with greater price differentials in individual utility GRCs or RDWs
Consider interaction of TOU rates with dynamic pricing, both high peak and low price/low net load

## Slide 9: Other Considerations
Utility loads have different generation coincident peaks and may also differ from CAISO system peak so TOU periods and seasons may not be the same
Similar variations may occur for distribution and should be studied
TOU periods should consider both and should not be different for generation vs. distribution as this would be very confusing to customers