## Slide 1: SCE Discussion on the Relationship Between NQC and EFC
February 9, 2015

## Slide 2: By Current Design, Effective Flexible Capacity (EFC) is Dependent on Net Qualifying Capacity (NQC)
D.14-06-050
  Storage and DR resources shall receive an EFC in accordance with the bundling principle, which holds that all Flexible RA resources must also qualify as System RA resources. In other words, storage and DR facilities wishing to qualify for Flexible RA must also be qualified for System RA, and must receive QC values as described previously. Additionally, PmaxRA values for Flexible RA shall be identical to those utilized in determining the resource’s System RA credit, and set according to the rules previously described.
  Dispatchable storage shall receive a QC in the same manner as other dispatchable resources, including testing and verification in CAISO operations. Because all RA resources must be able to operate for four or more consecutive hours, the storage operator must submit to the CAISO an output level (in MW) at which the resource is capable of discharging for four or more uninterrupted hours; this is defined to be its PmaxRA, the maximum output that can be considered for RA calculations.

## Slide 3: By Current Design, Effective Flexible Capacity (EFC) is Dependent on Net Qualifying Capacity (NQC)
All categories of resources describe the EFC as it relates to the NQC with one exception
Appendix B as adopted in D.14-06-050 describes the calculation of Effective Flexible Capacity (EFC)
  For storage and DR resources with positive generation only and start-up time < 90 minutes:
    EFC = Minimum of (NQC) and (PminRA + (180 minutes – Start-up Time) * ARRpos)
  For storage and DR facilities with positive generation only and start-up time > 90 minutes:
    EFC = Minimum of (NQC – PminRA) and (180 minutes * ARRpos)
  For storage or DR resources with negative generation only:
    EFC = Minimum of (Pdemandmin – PminRA) and (180 minutes * ARRneg), plus the absolute value of Pdemandmin iff 180 – (Pdemandmin – PminRA )/ARRneg ≥ shut-down time
  For storage or DR resources that have both curtail/discharge as well as load increase/charge components (PminRA < 0 and PmaxRA > 0):
    EFC = Minimum of (NQC) and (Psupplymin + 90 min * ARRpos) + Minimum of (– PminRA) and (– Pdemandmin + 90 minutes * ARRneg)

## Slide 4: Does EFC Need to be Limited by NQC?
SCE is concerned that as resources develop in the future, they may become more targeted in their capabilities
  It is possible that Demand Response and Energy Storage may configure their program or device to meet either the peak load need or the ramping need but may not meet both
The consequences of not meeting the peak load need and not meeting the system ramping needs are equally important from a reliability perspective
Given this, is it still advisable to limit a resources EFC by its NQC?